## Slide 1: GIS for Geoscientists Session 2: Beginner GIS
Presented by Nicholas Barber, 4th Year PhD Student at the University of Cambridge, U.K.
ndb38@cam.ac.uk | www.volcannick.com | https://github.com/ndb38 | Twitter @volcannick

## Slide 2: Feedback Form
Please fill out the feedback form Claire has sent around 

## Slide 3: Resources for further learning & Misc.

## Slide 4: Textbooks
Geospatial Analysis, de Smith (2020): https://www.spatialanalysisonline.com/HTML/index.html
Principles of Geographic Information Systems, Huisman & de By: https://webapps.itc.utwente.nl/librarywww/papers_2009/general/principlesgis.pdf

## Slide 5: #30DayMapChallenge

## Slide 7: Course Outline
Wed. Nov. 3rd: Session 1 – Principles for using GIS in the Geosciences
  Course Objectives
  Principles of GIS
  Tour of the Interface
Wed. Nov. 10th: Session 2 – Beginner GIS Exercises
  Guagua Pichincha Hazard Assessment (Exercise #1)
  Projections + Data Types
  Managing Layers, Manipulating Data, Designing Your Map
Wed. Nov 17th: Session 3 – Intermediate GIS Exercises
  Getting more out of GIS
  Geoprocessing, Spatial Analysis, Data Management, Advanced formatting, Geostatistics
Wed. Nov. 24th: Advanced GIS Exercises
  Peak into Advanced GIS
  Custom Actions , Model Builder, Python, Google Earth Engine, Databases

## Slide 8: Outline of today’s Session
Planning a project
Finding Data
Defining CRS/PCS
Initial Import + Projection
Georeferencing Images
Tracing Basemaps
Analysis: Geoprocessing, Statistics, Attributes
Visualization and Symbology***
Layout Design***

## Slide 9: Making a Plan

## Slide 10: Planning a QGIS Project
Need to think critically about where GIS fits in to your workflow
A few questions to ask yourself:
  What stage of my project am I in? And what value would GIS analyses add at different stages?
    E.g., in the planning stage, you might want a map and some prospect sites for outcrops. But in the analysis stage, you might want some specific spatial information about your study site
  What question am I trying to answer?
  Can this question be answered through other means?
  Is there data available for this? (short answer: YES)
    More important question: Where is the data I need??
  What steps do I need to take to answer this question?
  What coordinate/projection system should I use?
  How am I going to organize my data?

## Slide 11: Our Exercise Today
Focusing on Guagua Pichincha (GP), an active volcano adjacent to Ecuador’s capitol, Quito in the Andes
Our question: How many people are at risk of exposure to the different eruptive products of Guagua Pichincha Quito?
  This question encompasses two hazards: 1) lahars (volcanic mudflows) and 2) ash fall
Our role: GIS scientists asked to assess the risk of hazard exposure in the event of a major G.P. eruption
I selected this question for a few reasons:
  Require datasets that are readily accessibly
  Results verifiable based on previous research
  Analyses straightforward, but encompass the crucial “GIS Toolkit” you’ll get out of this course

## Slide 12: Volcanoes and History
Our volcano is essential in the story of Ecuadorian independence!
May 24th, 1822: The Battle of Pichincha
Image Credit: https://www.galapagosislands.com/blog/may-24th-holiday-batalla-de-pichincha/

## Slide 13: Importing + Reprojecting Data

## Slide 14: Importing Data
Format: SHP, GPKG, GeoTiff
Which layers to keep?
Renaming and resaving
Data specific tasks:
  Vector Data: Metadata
  Elevation data: Close Gaps + Hillshade
  CSV: Import
Reprojection

## Slide 15: Deciding on Coordinates and Projections

## Slide 16: We want something that’s accurate for our study area
Datum and Ellipsoid choice isn’t that practically important
We want a Latin American projection system, localized in Ecuador
Image source: EPSG Repository

## Slide 17: SIRGAS 2000/UTM Zone 17S
We are just in bounds of 1.0m accuracy SIRGAS 2000/17S
  EPSG 31977
Note: not the only choice we could make! There are many possibly options
  Decision based on locality (always better to fit with a projection suited to your part of the geoid) and widespread use – SIRGAS 2000 a standard CRS for South America
Image source: QGIS Projections Manager

## Slide 18: SIRGAS 2000
“The projection is reasonably accurate near the central meridian. Scale at an angular distance of 5° (in longitude) away from the central meridian is less than 0.4% greater than scale at the central meridian, and is about 1.54% at an angular distance of 10°.”
Image and Quote Source: https://en.wikipedia.org/wiki/Transverse_Mercator_projection

## Slide 19: Georeferencing

## Slide 20: What is Georeferencing?
Assignment of real world coordinates to pixels of an unreferenced raster
  Deccan Traps example from last time
Requires manually fixing “control points” between map and real spatial objects
BEST CONTROL POINTS:
  Riverheads
  Clear topographic features (ridge, unique landform, etc.)
  Intersections of lat/long grid lines
  Edge of map area
BAD CONTROL POINTS: Town names
Choice of transformation….
Thorough walk through: https://www.qgistutorials.com/en/docs/3/georeferencing_basics.html

## Slide 21
Map Source: Telenchana et al. (2019): The New Volcanic Hazard Map of Guagua Pichincha Volcano, Third Edition 2019.
https://www.researchgate.net/publication/336104232_The_New_Volcanic_Hazard_Map_of_Guagua_Pichincha_Volcano_Third_Edition_2019
11/10/21
20

## Slide 22: Tracing Basemap

## Slide 23: Creating New Features
Need to first define layer, then manually add points
  Note: image processing algorithm can do some of this work
NEXT account for tracing errors: I fixed my scale of tracing, so I know my error is between 10-50 m (USGS)
  ALWAYS KEEP SCALE IN MINDS
  We also have to account for distortion from georeferencing

## Slide 24: Errors

## Slide 25: Error Sources
Attribute data
  Unfortunately don’t know this at this time – what is the error in a census?
  Hazard Map doesn’t given an indication of error either, but doubtless there is some
Projection error (usually quite small)
  Estimated Error of SIRGAS is 1.0m (see EPSG website)
Georeferencing error: Error report suggests < 1 m
  However, given we didn’t know starting PCS, this is likely an underestimate – we can see some notable distortion
  Anything derived from basemap carries this georeferencing error forward
Base map error: USGS defines between 10-50m error in a map drawn between 1:20000-1:100000 scale
  We drew between these scales, so let's take the high end (50 m)

## Slide 26: Analysis

## Slide 27: Answering our question
How many people are at risk of exposure to the different eruptive products of Guagua Pichincha Quito?
Attribute Manipulation: How many people live in a canton?
Define provinces affected by ash and lahars
  Selection, Dissolving
Spatial Statistics: How many people in total?
  Exporting Statistics
Areal statistics: % Overlap in Lahars and Quito
  Proportion of population vulnerable to lahars

## Slide 28: Defining Key Terms
Spatial Statistics/Areal Statistics: Statistical + Analytical methods that add geographic space as a mathematical variable.
  Here, we are using simple statistical measures like the mean to describe a spatial feature: the extent to which a modeled volcanic hazard will affect Quito.
  But starting Friday, we will see how spatial statistics defines a unique and powerful branch of mathematics all its own.
Geoprocessing: Main spatial analysis workflows for topological problems. See next few slides for examples (http://webhelp.esri.com/arcgisdesktop/9.2/index.cfm?TopicName=An_overview_of_commonly_used_tools)

## Slide 29: Geoprocessing Tools
Note that raster files can be subjected to similar operations, they just get applied slightly differently.
Buffer
Append
Clip
Dissolve

## Slide 30: Geoprocessing Tools
Note that raster files can be subjected to similar operations, they just get applied slightly differently.
Union
Intersect
Erase
Identity

## Slide 31: Geoprocessing Tools
Note that raster files can be subjected to similar operations, they just get applied slightly differently.
Update
Symmetrical Difference

## Slide 32: Symbolizing

## Slide 33: Making the Data Look Nice
Do some of this formatting before editing the layout
Symbology:
  Making topography data look nice
  Stylizing vector data
    Fill
    Stroke
    Transparency
Label Making
  Easy Custom Labels + Memory

## Slide 34: Layout Management

## Slide 35: Layout
Elements we want:
  Main Map
  Regional Inset Map
  Legend
  North Arrow
  Scale bar
  Grid
  Labels for important features
  Text box summarizing findings
Things to keep in mind:
  Map Scale
  Locking of display
  Legend items
  Aesthetic value

## Slide 36: Thoughts for next time