## Slide 1: GIS for Geoscientists Session 1: Why GIS?
Presented by Nicholas Barber, 2nd Year PhD Student at the University of Cambridge, U.K.
ndb38@cam.ac.uk | www.volcannick.com | https://github.com/ndb38 | Twitter @volcannick

## Slide 2: Acknowledgements
Special thanks to Dr. Emma Liu for reaching out, developing the course with me, and putting together the logistics.

## Slide 3: Workshop Structure
Today: Session 1 – Principles and Motivation for GIS in the Geosciences
  Why GIS?
  Principles of GIS
  Getting acquainted with Quantum GIS?
Wednesday August 12th: Session 2 – Beginner GIS Exercise
  Tour of Interface
  Tutorial
Monday August 17th: Session 3 – Intermediate GIS Exercise
  Frontiers of GIS
  Geostatistics
  Python
  Data Management
  Advanced formatting
Wednesday August 19th: Scheduled “TA Hours” for 1-on-1 project advice

## Slide 5: Outline of Today’s Session
Objectives (10 Minutes)
My Background (10 Minutes)
Why GIS? (15 Minutes)
Principles of GIS (45 Minutes)
Whirlwind Intro to QGIS
(20 Minutes)

## Slide 6: Objectives
GIS = Geographic Information System
Definition:
“A GIS is a computer-based system to aid
in the collection, maintenance, storage,
analysis, output, and distribution of spatial
data and information.” – Paul Bolstad (GIS Fundamentals)

## Slide 7: Questions you may have going into this workshop:
What is GIS?
What can it do for me and my research?
What’s the best GIS software?
How do I learn the ins and outs?
Topics raised from surveys:
Best practices for setting up a new project?
How do I connect to and query a cloud-based spatial database?
Which coordinate system is preferred?
How do I create a map of my field site?
How do I use Sentinel-2 imagery?
How do I georeference a geological map?
How do I automate QGIS tasks
with python scripts?

## Slide 8: My goals over the next two weeks
Highlight what GIS can do for geoscientists
Outline the key principles of a geographic information system
Providing a fully guided GIS workflow template
Identify key areas of growth for GIS in geoscience research
https://github.com/ndb38/gis-for-geoscientists

## Slide 9: If you take nothing else away from this workshop….
GIS is a helpful tool in your workflow if you have data with a spatial dimension
GIS software lets you store, collect, analyze, and share spatial data
Modern GIS platforms like ArcMap and QGIS are all around workhorses – essential to tasks like spatial modeling, database management, cartography, geodesy, data visualization, hazard mitigation, and story telling
Learning the capabilities of GIS is acquired from repeated, often frustrating, trial and error with the hundreds of built-in tools
Studies should be designed with the GIS end user in mind!!!

## Slide 10: My Background
Past: B.S. Geoscience (Honors), Drexel University, USA
Current: PhD Earth Science, Cambridge, UK
Specialty Areas: Volcanology, Igneous Geochemistry
GIS Experience:
August 2014 - Present

## Slide 11: (Above) September 2018 to Present: Metals in Magmas Field Campaign, Java, Indonesia
(Right) May 2017 to August 2017: Deformation modeling with NOAA; Seafloor volcano Axial Seamount
(Below + Right) January 2016 to Present: Senior Project - Volume of Deccan Traps
(Right) August 2019 to Present): SlabMetals2 Glocal Arc Chemistry Database. Presenting at Goldschmidt!

## Slide 12: Why GIS?
Motivations for the strapped-for-time earth scientist

## Slide 13: Four reasons to use GIS
Job Prospects
Advancing your analysis
Making your data reusable
Story telling

## Slide 14: Job Prospects
Geospatial industry projected to grow to a value of $19 billion USD by 2024
  Compound annual growth rate (CAGR) of over 10%
  Most of this growth in North America
Employment for GIS specialists outstripping average employment growth
Geological Society of London highlights GIS alongside drawing software and programming skills as essential skills in careers for geologists

## Slide 15: Job Prospects
Learning how to properly use GIS takes time and patience. That translates to value for any employer (academic private, public)
Positioning yourself as a geologist with GIS awareness increases your utility in any organization

## Slide 16: Advancing your analysis
Economic Geology:
  Using satellite imagery to narrow search for mineral resources
  Determining cost/environmental impact of a new mine (water resources, accessibility, topography, water table, population centers, municipal boundaries)
Volcanology
  Mapping risk posed by different eruption scenarios
Environmental Geology
  Modeling the risk posed by a pollutant at a great distance from pollution source
Sedimentology
  Mapping known outcrops to determine where the same formation will appear outside study area
Geophysics + Structural geology
  Integrate stress n models and seismic focal mechanisms with known geology + chemistry

## Slide 17: Example: SlabMetals2
Data sources: GEOROC, Hayes et al. 2018 (Science), Szwilllus et al. 2019 (JGR), Barber et al. 2020 (in prep.)

## Slide 18: Making Data Reusable
As earth scientists, everything we do is spatial
Open Data and Data Reproducibility one of the biggest concerns/frontiers in science today
If you aren’t building spatial metadata/analyses into your workflow, your work isn’t reproducible by other earth scientists!

## Slide 19: Example: Stratigraphy of the Deccan Traps

## Slide 20: Example: Stratigraphy of the Deccan Traps

## Slide 21: Story Telling + Communication
Underlying link of our data to the wider world makes for compelling stories
Integrating GIS into your research lets you tell stories rooted in place, time, and culture
Story Maps from ESRI:
  ESRI (ArcGIS) has developed digital story telling format the leverages this capacity
  Alternative way to present your research
  Let the maps tell your story

## Slide 22: JHU COVID Hub

## Slide 23: Principles of GIS
Working Principles  Data Management  Projections  Data Types  Errors  Layout  Software

## Slide 24: Data Management
GIS data is diffuse, found in about 1000 different repositories
  Governmental
  Nonprofit
  Educational
  Research
    Individual papers
    Consortiums
  Private
File structure complex – one elevation dataset may have 6+ individual files, that all get compiled upon use in software
File size can be massive: my master elevation dataset for Western India is several gigabytes!
In a GIS software, proliferation of “layers” mandates good naming schemes, efficient data storage, and logical file structure

## Slide 25: LAWS OF GIS Law 1: Pick a naming scheme, file structure, data format that suits you. Keep it consistent and document every choice you make throughout a project!

## Slide 26: Coordinates & Projections
We use coordinates to define the “where” on a map
  Easting and Northing
  X and Y
  Latitude and Longitude
However, defining where something is may not be straightforward
  Maps are a flat surface, and the earth is 3D. There is inherently distortion converting coordinates from 3D to 2D
  Need to consider that the Earth is not a sphere
  Error in spatial measurements
  Physical location of an object changes through time

## Slide 27: Coordinates & Projections
The coordinates of a spatial object depends on
  A reference system (or datum) defining shape of the Earth
  A projection, or mathematical transformation from spherical --> Cartesian coordinates
  The error inherent in the measurement of the feature
  The change of position with respect to time or space
In defining a coordinate system, you essentially want to be able to convert between X, Y, Z in 2D space and Lat, Long, Height in spherical space
No spatial analysis can be done accurately without this very important step!!

## Slide 28: Early + Modern attempts to define the shape of the Earth
Pythagoras, Aristotle reasoned Earth must be a sphere
Eratosthenes (276 -194 BCE, Libya) measured circumference of the Earth to within 4% of modern accepted value
Ptolemy (90-168 CE, Egypt) set the accepted standard shape of the Earth
Aryabhatta (476-550 CE, Bihar, India) got within 70 miles of correct equatorial circumference
Abu Rayhan Biruni (973-1048 CE, Uzbekistan) held most accurate measurements of Earth’s radius until the Enlightenment in Europe
18th century saw geographers characterize Earth as an ellipsoid rather than a sphere
Clarke and Bessel ellipsoids popular in 19th century NA and Europe, respectively
“We define the geoid as the three-dimensional
equipotential surface, along which the
pull of gravity is a specified constant” – Bolstad Ch. 3

## Slide 29: Development of GPS – Glady West
Developed the geoid model that went in to
Building the first global position system in the 1980s

## Slide 30: Coordinates & Projections
We reference the geoid as our “zero-height” 3D baseline for spatial locations on, above, or below Earth
  Geoid defined by gravity, and is fixed regardless of atmospheric or oceanic processes
We start with horizontal and vertical reference systems, or datums, to define the position of an object relative to the ellipsoid
  There are several main ellipsoids to choose from (e.g. WGS84)
Next, we define the projection system, which converts our ellipsoidally-referenced positions to a flat, 2D map.
  This is where the dizzying array of projection systems comes in!
  Choice of projection has been a topic of recent debate and controversy

## Slide 31: www.thetruesizeof.com

## Slide 32: Law 2 : Known your coordinate system and make every layer in a project use the same system!! This needs to be done prior to any analysis

## Slide 33: Data Types
VECTOR DATA
  Essentially, a spreadsheet that is visualized by a geometry
  Geometries include Point, Line, Polygon, Multiline, Multishape, etc.
  Common format: Shapefile (.shp), Geopackage (.gpkg), File Geodatabase, KML, CSV, GeoJSON
  Relevant data stored in an ATTRIBUTE TABLE
RASTER DATA
  Digital image, with data stored in discrete cells of a specific resolution & spectral value
  Efficient way to store and present large amount of data
  Common formats: GeoTIFF, ESRI Grid, GDAL VRT, etc.
  Common uses: Elevation, satellite data

## Slide 34: Law 3 : Design a project with these data types in mind!

## Slide 35: Errors
Sources of error abound in a GIS:
  Accuracy of datum and projection system
  Positional accuracy of data
    Measurement accuracy
    Map Scale accuracy
    Tied to original scale at which data was mapped, not the scale at which you do the analyses
  Quantitative accuracy of attribute data
  Conceptual accuracy
    How accurate it is it to cluster features into different groups?
  Knowledge of User
  “Human Error”
    For example: estimated error introduced by manually tracing geological boundary in a GIS

## Slide 36: Law 4 : Enumerate error sources at the start of a project, and document error + error propagation as you go!

## Slide 37: Layout + Design
Essential, and one of the most challenging/impenetrable aspects of GIS
Based on principles of design + cartography
  Need visualization to be as elegant as it is accurate
Remember data reusability!
  Underlying data accessible and well documented

## Slide 39: Law 5 : No one will read your map if it’s not designed well – treat any GIS output as you would any figure in a paper!

## Slide 40: Software: The Two Juggernauts
ESRI’s ArcMap
Propietary & Industry Standard
The Gold Standard
Comes with a range of products, like Story Maps, ArcGIS Online, Customer support, 3D Viz, other Advanced tools
Data formats are often proprietary and closed-source
Algorithms + data structure can be opaque and hard to reference
Quantum GIS (QGIS)
Open source, community driven
Not as feature rich but a fast-rising competitor to Arc
Integrated with other open source projects like SAGA, GDAL, Python, PostGreSQL, GRASS GIS, etc.
Can read/process almost any data type
Interface can be clunky
Software dependency issues

## Slide 41: Software: The Two Juggernauts
ESRI’s ArcMap
Proprietary & Industry Standard
The Gold Standard
Comes with a range of products, like Story Maps, ArcGIS Online, Customer support, 3D Viz, other Advanced tools
Data formats are often proprietary and closed-source
Algorithms + data structure can be opaque and hard to reference
Quantum GIS (QGIS)
Open source, community driven
Not as feature rich but a fast-rising competitor to Arc
Integrated with other open source projects like SAGA, GDAL, Python, PostGreSQL, GRASS GIS, etc.
Can read/process almost any data type
Interface can be clunky
Software dependency issues

## Slide 42: Law 6 : Keep in mind the audiences and limitations of each software. Make your software choice early, and stick with it!

## Slide 43: Introducing QGIS 3.10
A fly-by-tour of the best open source GIS software – Quantum GIS

## Slide 44: Overview of QGIS 3.10
Installation
Opening up for the first time
Introduce layout
  Browser
  Layers
  Various menus
  Processing
  Plugins
  Layout
  Project Settings
  Properties
  Symbology

## Slide 45: On to the real thing!