## Slide 1: GIS For Dummies Session 2: Live Demo
Presented by Nicholas Barber, 2nd Year PhD Student at the University of Cambridge, U.K.
ndb38@cam.ac.uk | www.volcannick.com | https://github.com/ndb38 | Twitter @volcannick

## Slide 2: Workshop Structure
Today: Session 1 – Principles and Motivation for GIS in the Geosciences
  Why GIS?
  Principles of GIS
  Getting acquainted with Quantum GIS?
Wednesday June 17th: Session 2 – Tutorial + Guagua Pichincha Exercise
  Tour of Interface
  Tutorial
Monday June 29th: Session 3 (GIS for the Intrepid) - Advanced GIS
  Frontiers of GIS
    Geostatistics
    Python
    Data Management
    Advanced formatting
Wednesday July 1st: Scheduled “TA Hours” for 1-on-1 project advice

## Slide 3: Refresher on Interface
Queuing up plugins we'll need, refamiliarizing ourselves with the interface

## Slide 4: Textbook Info to Come

## Slide 5: Outline of today’s demonstration
Planning a project
Finding Data
Defining CRS/PCS
Initial Import + Projection
Georeferencing Images
Tracing Basemaps
Analysis: Geoprocessing, Statistics, Attributes
Visualization and Symbology
Layout Design

## Slide 6: Making a Plan

## Slide 7: Planning a QGIS Project
Need to think critically about where GIS fits in to your workflow
A few questions to ask yourself:
  What stage of my project am I in? And what value would GIS analyses add at different stages?
    E.g., in the planning stage, you might want a map and some prospect sites for outcrops. But in the analysis stage, you might want some specific spatial information about your study site
  What question am I trying to answer?
  Can this question be answered through other means?
  Is there data available for this? (short answer: YES)
    More important question: Where is the data I need??
  What steps do I need to take to answer this question?
  What coordinate/projection system should I use?
  How am I going to organize my data?

## Slide 8: Our Exercise Today
Focusing on Guagua Pichincha (GP), an active volcano adjacent to Ecuador’s capitol, Quito in the Andes
Our question: How many people are at risk of exposure to the different eruptive products of Guagua Pichincha Quito?
  This question encompasses two hazards: 1) lahars (volcanic mudflows) and 2) ash fall
I selected this question for a few reasons:
  Require datasets that are readily accessibly
  Results verifiable based on previous research
  Analyses straightforward, but encompass the crucial “GIS Toolkit” you’ll get out of this course

## Slide 9: Our Exercise Today
Structure today:
  Live Demo will showcase tools and parameters needed to answer this question
  Will be accompanied by discussions with these slides
  IN DEVELOPMENT: By the end of the four-part workshop, I’ll create detailed guides in PDF format, describing this exercise workflow step by step.
Skills you will get out of this exercise: project design, data sourcing, projecting vector and raster data, importing data, setting up interface, file management, basic vector analysis, attribute table calculations, spatial statistics, georeferencing, creating new features, symbology + visualization, layout management.
Next time we will use G.P. and this region of Ecuador for some more advanced statistical and analytical procedures
WILL ASK CAT TO SOLICIT FEEDBACK AFTER THIS WEEK

## Slide 10: Finding Data

## Slide 11: Where in the world do I find data?
Think in detail about our question: what do we need to have?
  Information on volcano
    Geology
    Estimated hazards
      Location
      Severity
    Geochemistry/Geophysics?
  Information on surrounding population
    Infrastructure?
    Hydrology
    Municipal boundaries
    Location of Major population centers
    Population #
      Demography?
  Information on topography

## Slide 12: Where in the world do I find data?
Think in detail about our question: what do we need to have?
  Information on volcano
    Geology
    Estimated hazards
      Location
      Severity
    Geochemistry/Geophysics?
  Information on surrounding population
    Infrastructure?
    Hydrology
    Municipal boundaries
    Location of Major population centers
    Population #
      Demography?
  Information on topography

## Slide 13: Generic Datasets (Example): https://geodata.tufts.edu

## Slide 14: Other Data Sources
Economic Geology: https://mrdata.usgs.gov/general/map-global.html
Similar generic info: http://hgl.harvard.edu:8080/opengeoportal/
Humanitarian/land use data: https://geoportal.landportal.org/?gclid=CjwKCAjw_qb3BRAVEiwAvwq6Vgusj8dZX1TuJTa3ipj7r6hEaFvMbdN-ZZJ2ekZ8iNdt-FZZJnmMHhoCAWUQAvD_BwE
USGS Earth Explorer: https://earthexplorer.usgs.gov
ESRI Hub: https://hub.arcgis.com/search
Natural Earth: http://www.naturalearthdata.com/downloads/
NASA Socioeconomic data: https://sedac.ciesin.columbia.edu
LIDAR Data: https://opentopography.org
UN Data: http://geodata.grid.unep.ch
Pop and Enviro Data: https://terra.ipums.org

## Slide 15: Deciding on Coordinates and Projections

## Slide 16: Importing + Reprojecting Data

## Slide 17: We want something that’s accurate for our study area
Datum itself isn’t that important – one of the most common is GRS80
We want a Latin American projection system, localized in Ecuador

## Slide 18: Importing Data
Format: SHP, GPKG, GeoTiff
Which layers to keep?
Renaming and resaving
Data specific tasks:
  Vector Data: Metadata
  Elevation data: Close Gaps + Hillshade
  CSV: Import
Reprojection

## Slide 19: SIRGAS 2000/UTM Zone 17S
We are just in bounds of 1.0m accuracy SIRGAS 2000/17S
  EPSG 31977
Note: not the only choice we could make! There are many possibly options
  Decision based on locality (always better to fit with a projection suited to your part of the geoid) and widespread use – SIRGAS 2000 a standard CRS for South America

## Slide 20: SIRGAS 2000
“The projection is reasonably accurate near the central meridian. Scale at an angular distance of 5° (in longitude) away from the central meridian is less than 0.4% greater than scale at the central meridian, and is about 1.54% at an angular distance of 10°.”

## Slide 21: Georeferencing

## Slide 22: What is Georeferencing?
Assignment of real world coordinates to pixels of an unreferenced raster
  Deccan Traps example from last time
Requires manually fixing “control points” between map and real spatial objects
BEST CONTROL POINTS:
  Riverheads
  Clear topographic features (ridge, unique landform, etc.)
  Intersections of lat/long grid lines
  Edge of map area
BAD CONTROL POINTS: Town names
Choice of transformation….
Thorough walk through: https://www.qgistutorials.com/en/docs/3/georeferencing_basics.html

## Slide 24: Tracing Basemap

## Slide 25: Creating New Features
Need to first define layer, then manually add points
  Note: image processing algorithm can do some of this work
NEXT account for tracing errors: I fixed my scale of tracing, so I know my error is between 10-50 m (USGS)
  ALWAYS KEEP SCALE IN MINDS
  We also have to account for distortion from georeferencing

## Slide 26: Errors

## Slide 27: Error Sources
Attribute data
  Unfortunately don’t know this at this time – what is the error in a census?
  Hazard Map doesn’t given an indication of error either, but doubtless there is some
Projection error (usually quite small)
  Estimated Error of SIRGAS is 1.0m (see EPSG website)
Georeferencing error: Error report suggests < 1 m
  However, given we didn’t know starting PCS, this is likely an underestimate – we can see some notable distortion
  Anything derived from basemap carries this georeferencing error forward
Base map error: USGS defines between 10-50m error in a map drawn between 1:20000-1:100000 scale
  We drew between these scales, so let's take the high end (50 m)

## Slide 28: Analysis

## Slide 29: Answering our question
How many people are at risk of exposure to the different eruptive products of Guagua Pichincha Quito?
Attribute Manipulation: How many people live in a canton?
Define provinces affected by ash and lahars
  Selection, Dissolving
Spatial Statistics: How many people in total?
  Exporting Statistics
Areal statistics: % Overlap in Lahars and Quito
  Proportion of population vulnerable to lahars

## Slide 30: Symbolizing

## Slide 31: Making the Data Look Nice
Do some of this formatting before editing the layout
Symbology:
  Making topography data look nice
  Stylizing vector data
    Fill
    Stroke
    Transparency
Label Making
  Easy Custom Labels + Memory

## Slide 32: Layout Management

## Slide 33: Layout
Elements we want:
  Main Map
  Regional Inset Map
  Legend
  North Arrow
  Scale bar
  Grid
  Labels for important features
  Text box summarizing findings
Thigs to keep in mind:
  Map Scale
  Locking of display
  Legend items
  Aesthetic value

## Slide 34: Thoughts for next time